## Slide 1: Internet Of Things Hands on Workshop
DAY 1

## Slide 2
Like every other IoT workshop, I’ll ask the same…
What is IoT?

## Slide 3
In the term, Internet of Things, “Thing” refers to any object. Eg: Table, fan, computer, phones, TV, AC, etc.
What about Sensors? Anything and Everything that connects to the Internet is a part of IoT. An object may or may not have a sensor.
Need of Internet? Connect every device with each other (inter-connect), to make a mesh of Connectivity among devices as well.
In IoT, things need not be connected with cloud. They could form an IoT, even if it is running locally (LAN).

## Slide 6
Introduction to IoT
IoT Concepts
Examples
Branches of IoT
Levels of IoT
Communication Protocols
Types of IoT Protocols
IoT Communication Protocols
Serial Communication
WebServer on ESP32
Create an ESP32 WebServer
Host images from ESP32 Memory (using SPIFFS)
IoT Platforms
Use Blynk-cloud with API to control ESP32
Use thingspeak API to get data of ESP32
Introduction to Arduino IoT Cloud
Store and Visualize Data
Store data in Google Sheet
Create a google chart with the data
Create your Own IoT Service
Using Firebase to store data in JSON
Using self-developed REST API server - Data, chart
Introduction to Toit
What is Toit?
Toit language - CLI
Control-Monitor everything with toit API
Over the Air Updates

## Slide 10
InterConnected Humans

## Slide 11
Top Examples
Inventory-tracking systems (workplace, logistics, import-export, etc)
Machines in Manufacturing Factories
Tags and sensors for security
HealthCare system
Appliance Control (home-automation, smart fridge, toaster, etc)
Environmental data gathering (weather, air quality, etc)

## Slide 13
Branches of IoT
Data Centre
Inventory Management
Security
Mobile Device (Portable/wearable)
Asset and Fleet Management
HealthCare
Retail/Commercial Products

## Slide 14
Sections in IoT network
Database: Database can be either local or in the cloud and stores the data generated by the IoT device.
Web Service: Web services serve as a link between the IoT device, application, database and analysis components. Web service can be either implemented using HTTP and REST principles (REST service) or using WebSocket protocol (WebSocket service).
Analysis Component: The Analysis Component is responsible for analyzing the IoT data and generate results in a form which are easy for the user to understand.
Application: IoT applications provide an interface that the users can use to control and monitor various aspects of the IoT system. Applications also allow users to view the system status and view the processed data.

## Slide 16
IoT Level 1
A level-1 IoT system has a single node/device that performs sensing and/or actuation, stores data, performs analysis and hosts the application.
Suitable for modelling low-cost and low-complexity solutions where the data involved is not big and the analysis requirements are not computationally intensive.

## Slide 17
IoT Level 2
A level-2 IoT system has a single node that performs sensing and/or actuation and local analysis.
Data is stored in the cloud and application is usually cloudbased.
Suitable for solutions where the data involved is big, however, the primary analysis requirement is not computationally intensive and can be done locally itself.

## Slide 18
IoT Level 3
A level-3 IoT system has a single node. Data is stored and analyzed in the cloud and application is cloudbased.
Level-3 IoT systems are suitable for solutions where the data involved is big and the analysis requirements are computationally intensive.

## Slide 19
IoT Level 4
A level-4 IoT system has multiple nodes that perform local analysis. Data is stored in the cloud and application is cloud-based.
Level-4 contains local and cloudbased observer nodes which can subscribe to and receive information collected in the cloud from IoT devices.
Level-4 IoT systems are suitable for solutions where multiple nodes are required, the data involved is big and the analysis requirements are computationally intensive.

## Slide 20
IoT Level 5
A level-5 IoT system has multiple end nodes and one coordinator node.
The end nodes that perform sensing and/or actuation.
Coordinator node collects data from the end nodes and sends to the cloud.
Data is stored and analyzed in the cloud and application is cloud-based.
Level-5 IoT systems are suitable for solutions based on wireless sensor networks, in which the data involved is big and the analysis requirements are computationally intensive.

## Slide 21
IoT Level 6
A level-6 IoT system has multiple independent end nodes that perform sensing and/or actuation and send data to the cloud.
Data is stored in the cloud and application is cloud-based.
The analytics component analyses the data and stores the results in the cloud database.
The results are visualized with the cloud-based application.
The centralized controller is aware of the status of all the end nodes and sends control commands to the nodes.

## Slide 22
Type of IoT Protocol
IoT Network
IoT Data

## Slide 23
IoT Networks
1. Wifi
Standard - Based on IEEE 802.11n
Frequencies - 2.4 GHz and 5 GHz bands
Range- Approx. - 50 - 100 meters
Data Rates - 600 Mbps maximum, the most common is 150-200 Mbps.

## Slide 24
IoT Networks
2. Bluetooth
Standard - Bluetooth 4.2 core specification
Frequencies - 2.4 GHz (ISM)
Range- Approx. - 10meter - 50 meters
Data Rates - 1MBps(Smart/BLE)

## Slide 25
IoT Networks
3. Zigbee
Standard - Zigbee 3.0 based on IEEE802.15.4
Frequencies - 2.4 GHz (ISM)
Range- Approx. - 10 - 100 meters
Data Rates - 250KBps

## Slide 26
IoT Networks
4. Cellular
Standard - GSM/GPRS/EDGE(2G), UMTS/HSPA(3G), LTE(4G)
Frequencies - 900/1800/1900/2100MHz
Range- Approx. - 35km max for GSM, 200 km max for HSPA
Data Rates - 35 – 170 KBps

## Slide 27
IoT Networks
5. LoRa
Standard- LoRa WAN
Frequencies- Various
Range- Approx. – 2.5km (Urban) and 15km (SubUrban)
Data Rates - 0.3 – 50 KBps

## Slide 28
IoT Networks
6. SigFox
Standard - SigFox
Frequencies - 900 MHz
Range- Approx. – 3 - 10km (Urban) and 30 - 50km (SubUrban)
Data Rates - 10 – 1000 Bps

## Slide 29
IoT Data Protocols
REST API- Application programming interface (API or web API) that conforms to the constraints of REST architectural style and allows for interaction with RESTful web services.
WebSocket- A computer communications protocol, providing full-duplex communication channels over a single TCP connection.
MQTT- MQTT is a lightweight, publish-subscribe network protocol that transports messages between devices. The protocol usually runs over TCP/IP, however, any network protocol that provides ordered, lossless, bi-directional connections can support MQTT.
Others - CoAP, AMQP, XMPP are some of the popular IoT data protocols.

## Slide 30
Device Communication
Serial Communication - Uses one or two transmission lines to send and receive data, and that data is continuously sent and received one bit at a time.
SPI Communication - Devices are in a master-slave relationship. The master is the controlling device (usually a microcontroller), while the slave (usually a sensor, display, or memory chip) takes instruction from the master.
I2C Communication - I2C combines the best features of SPI and UARTs. You can connect multiple slaves to a single master (like SPI) and you can have multiple masters controlling single, or multiple slaves.

## Slide 31
What is ESP32?

## Slide 32
Espressif - 32
ESP32 is a system on a chip that integrates the following features:
Wi-Fi (2.4 GHz band)
Bluetooth
Dual high performance Xtensa® 32-bit LX6 CPU cores
Ultra Low Power co-processor
Multiple peripherals
ESP32 provides a robust, highly integrated platform, which helps meet the continuous demands for efficient power usage, compact design, security, high performance, and reliability.

## Slide 33
ESP32 vs ESP32 Dev Board

## Slide 34
shorturl.at/hlLV7
Access all Code (Web Server on ESP32)

## Slide 35
IoT Platforms
Blynk IoT
ThingSpeak API
Arduino IoT Cloud

## Slide 36
shorturl.at/rvyR0
Access all Code (IoT Platforms)

## Slide 37
Arduino IoT Cloud
Arduino IoT Cloud is an application that helps makers build connected objects in a quick, easy and secure way. You can connect multiple devices to each other and allow them to exchange real-time data. You can also monitor them from anywhere using a simple user interface. Arduino has taken a step forward to keep IoT as simple and reachable as possible. Initially, IoT Cloud was available only to the Arduino Boards, but now, it even provides Web Sketches for other third-party boards like ESP8266 / 32, LoRaWAN as well.

## Slide 38
https://docs.arduino.cc/cloud/iot-cloud/tutorials/esp-32-cloud
Arduino IoT Cloud

## Slide 39
TASK (1/5)
Create a Flow Diagram of an IoT Network, in a Forest
Add necessary devices and sensors required, to be used in the Wildlife of Forest.
Concern on Climate Monitor (fire, moisture, rain, etc), Wild Animal movement, etc.
Mention the IoT Level used, with an explanation on the flow. State reasons for each block.
Make sure any device/sensor MUST not link directly to any Animal or Organism.
Scores based upon Creativity and Uniqueness.
Use Pen-Paper/Photoshop/FlowChartBuilder/Anything. No restrictions on that.

## Slide 40
TASK (2/5)
Use the Blynk App and create a Basic Home Automation Control. Follow the Configuration :
V0 – Button
V1 – Slider (0 - 1023) – Show Value
V2 – Step H (0 - 1023) – Show Value – icon(+/-)
V3 – Value Display (0 – 255)
V4 – Gauge (0 - 1023) - ºC
V5 – LED
Copy the Auth Token of the Project and Paste it on the WebPage and click Enter.
Send a screenshot of the Blynk App with the Configuration working.
Blynk_HomeAutomation_Verifier.html

## Slide 41
Submission Link
https://forms.gle/CG7B44EAnnkKXZZ48

## Slide 42
Thank You
Reach me in the below Socials:
linkedin.com/in/akshayansinha/
hackster.io/akshayansinha
instagram.com/akshayansinha/
github.com/hippyaki
akshayan.sinha@gmail.com
LinkedIn -
Hackster -
Instagram -
Github -
Mail -

## Slide 43
Meet you on 2nd November.